# BGM220P Zephyr Board Porting Guide
## Overview
The BGM220P is a Bluetooth Low Energy module based on the Silicon Labs EFR32BG22 SoC. Since Zephyr already supports EFR32BG22, we can create a board port by leveraging existing SoC support.
## Prerequisites
- Zephyr development environment set up
- BGM220P module datasheet and schematics
- Understanding of the module's pin configuration
- Development board or custom PCB with BGM220P
## Step-by-Step Porting Process
### Step 1: Create Board Directory Structure
# Navigate to your Zephyr boards directory
cd ~/zephyrproject/zephyr/boards

# Create board directory structure (new hardware model)
mkdir -p silabs/bgm220p_efr32bg22
cd silabs/bgm220p_efr32bg22
### Step 2: Create Board Configuration Files
#### board.yml - Board Definition
# boards/silabs/bgm220p_efr32bg22/board.yml
identifier: bgm220p_efr32bg22
name: BGM220P EFR32BG22
type: mcu
arch: arm
toolchain:
  - zephyr
  - gnuarmemb
  - xtools
supported:
  - gpio
  - i2c
  - spi
  - uart
  - adc
  - pwm
  - watchdog
  - counter
  - bluetooth
vendor: silabs
socs:
  - name: efr32bg22
    variants:
      - name: efr32bg22c224f512im40
#### bgm220p_efr32bg22_defconfig - Default Configuration
# boards/silabs/bgm220p_efr32bg22/bgm220p_efr32bg22_defconfig

# SoC Configuration
CONFIG_SOC_SERIES_EFR32BG22=y
CONFIG_SOC_EFR32BG22C224F512IM40=y

# Board Configuration
CONFIG_BOARD_BGM220P_EFR32BG22=y

# CPU Configuration
CONFIG_ARM_MPU=y
CONFIG_HW_STACK_PROTECTION=y

# Clock Configuration
CONFIG_CLOCK_CONTROL=y
CONFIG_CMU_HFCLK_HFXO=y
CONFIG_CMU_HFXO_FREQ=38400000

# Console Configuration
CONFIG_CONSOLE=y
CONFIG_UART_CONSOLE=y
CONFIG_SERIAL=y

# GPIO Configuration
CONFIG_GPIO=y

# Enable Bluetooth
CONFIG_BT=y
CONFIG_BT_PERIPHERAL=y
CONFIG_BT_CENTRAL=y
CONFIG_BT_GATT_DM=y
CONFIG_BT_SETTINGS=y
CONFIG_BT_HOST_CRYPTO=y

# Flash and NVS
CONFIG_FLASH=y
CONFIG_FLASH_MAP=y
CONFIG_NVS=y
CONFIG_SETTINGS=y
CONFIG_SETTINGS_NVS=y

# Bootloader
CONFIG_BOOTLOADER_MCUBOOT=y
#### bgm220p_efr32bg22.dts - Device Tree Source
// boards/silabs/bgm220p_efr32bg22/bgm220p_efr32bg22.dts

/dts-v1/;
#include <silabs/efr32bg22c224f512im40.dtsi>
#include <zephyr/dt-bindings/input/input-event-codes.h>
#include <zephyr/dt-bindings/pwm/pwm.h>

/ {
    model = "Silicon Labs BGM220P EFR32BG22";
    compatible = "silabs,bgm220p_efr32bg22", "silabs,efr32bg22";

    chosen {
        zephyr,console = &usart0;
        zephyr,shell-uart = &usart0;
        zephyr,sram = &sram0;
        zephyr,flash = &flash0;
        zephyr,code-partition = &slot0_partition;
        zephyr,bt-hci = &bt_hci_silabs;
    };

    /* Module-specific aliases */
    aliases {
        led0 = &led0;
        sw0 = &button0;
        watchdog0 = &wdog0;
        spi-flash0 = &mx25r8035f;
    };

    leds {
        compatible = "gpio-leds";
        led0: led_0 {
        gpios = <&gpioa 4 GPIO_ACTIVE_HIGH>;
        label = "LED 0";
        };
    };

    buttons {
        compatible = "gpio-keys";
        button0: button_0 {
        gpios = <&gpioa 5 GPIO_ACTIVE_LOW>;
        label = "User Push Button 0";
        zephyr,code = <INPUT_KEY_0>;
        };
    };

    /* Power supply configuration */
    vdd: vdd {
        compatible = "regulator-fixed";
        regulator-name = "VDD";
        regulator-min-microvolt = <3300000>;
        regulator-max-microvolt = <3300000>;
        regulator-always-on;
    };
};

/* UART Configuration for Debug */
&usart0 {
    status = "okay";
    current-speed = <115200>;
    pinctrl-0 = <&usart0_default>;
    pinctrl-names = "default";
};

/* GPIO Configuration */
&gpioa {
    status = "okay";
};

&gpiob {
    status = "okay";
};

&gpioc {
    status = "okay";
};

&gpiod {
    status = "okay";
};

/* I2C Configuration */
&i2c0 {
    status = "okay";
    pinctrl-0 = <&i2c0_default>;
    pinctrl-names = "default";
};

/* SPI Configuration */
&spi0 {
    status = "okay";
    pinctrl-0 = <&spi0_default>;
    pinctrl-names = "default";

    mx25r8035f: mx25r8035f@0 {
        compatible = "jedec,spi-nor";
        reg = <0>;
        spi-max-frequency = <80000000>;
        size = <0x800000>;
        jedec-id = [c2 28 14];
        sfdp-bfp = [
        e5 20 f1 ff ff ff ff 03 44 eb 08 6b 08 3b 04 bb
        ee ff ff ff ff ff 00 ff ff ff 00 ff 0c 20 0f 52
        10 d8 00 ff 23 72 f5 00 82 ed 04 cc 44 83 68 44
        30 b0 30 b0 f7 c4 d5 5c 00 be 29 ff f0 d0 ff ff
        ];
    };
};

/* Flash partitions */
&flash0 {
    partitions {
        compatible = "fixed-partitions";
        #address-cells = <1>;
        #size-cells = <1>;

        /* Reserve 48 kB for the bootloader */
        boot_partition: partition@0 {
        label = "mcuboot";
        reg = <0x0 0x0000c000>;
        read-only;
        };

        /* Reserve 464 kB for the application in slot 0 */
        slot0_partition: partition@c000 {
        label = "image-0";
        reg = <0x0000c000 0x00074000>;
        };

        /* Reserve 4 kB for the scratch partition */
        scratch_partition: partition@80000 {
        label = "image-scratch";
        reg = <0x00080000 0x00001000>;
        };

        /* Reserve 4 kB for storage */
        storage_partition: partition@81000 {
        label = "storage";
        reg = <0x00081000 0x00001000>;
        };
    };
};

/* Bluetooth Configuration */
&bt_hci_silabs {
    status = "okay";
};

/* Watchdog */
&wdog0 {
    status = "okay";
};

/* Random Number Generator */
&trng0 {
    status = "okay";
};

/* Pinctrl Configuration */
&pinctrl {
    /* UART pins */
    usart0_default: usart0_default {
        group1 {
        psels = <GECKO_PSEL(UART_TX, A, 5)>,
        <GECKO_PSEL(UART_RX, A, 6)>;
        };
    };

    /* I2C pins */
    i2c0_default: i2c0_default {
        group1 {
        psels = <GECKO_PSEL(I2C_SDA, C, 1)>,
        <GECKO_PSEL(I2C_SCL, C, 0)>;
        };
    };

    /* SPI pins */
    spi0_default: spi0_default {
        group1 {
        psels = <GECKO_PSEL(SPI_MOSI, C, 0)>,
        <GECKO_PSEL(SPI_MISO, C, 1)>,
        <GECKO_PSEL(SPI_CLK, C, 2)>,
        <GECKO_PSEL(SPI_CS, C, 3)>;
        };
    };
};
#### board.cmake - Build Configuration
# boards/silabs/bgm220p_efr32bg22/board.cmake

# Flash using J-Link
board_runner_args(jlink "--device=EFR32BG22CxxxF512")
board_runner_args(jlink "--reset-after-load")

# Flash using OpenOCD
board_runner_args(openocd --target-file=${ZEPHYR_BASE}/boards/silabs/bgm220p_efr32bg22/support/openocd.cfg)

# Include standard board runners
include(${ZEPHYR_BASE}/boards/common/jlink.board.cmake)
include(${ZEPHYR_BASE}/boards/common/openocd.board.cmake)
### Step 3: Create Support Files
#### support/openocd.cfg - OpenOCD Configuration
# boards/silabs/bgm220p_efr32bg22/support/openocd.cfg

source [find interface/jlink.cfg]
transport select swd

source [find target/efr32.cfg]

# BGM220P specific configuration
set CHIPNAME efr32bg22
set CPUTAPID 0x2ba01477

# Flash configuration
flash bank $_CHIPNAME.flash efr32 0x00000000 0 0 0 $_TARGETNAME
flash bank $_CHIPNAME.userdata efr32 0x0fe00000 0 0 0 $_TARGETNAME

# Reset configuration
reset_config srst_only

# BGM220P has 512KB flash, 32KB RAM
set FLASH_SIZE 0x80000
set RAM_SIZE 0x8000
### Step 4: Create Documentation
#### doc/index.rst - Board Documentation
.. _bgm220p_efr32bg22:

BGM220P EFR32BG22
##################

Overview
********

The BGM220P is a Bluetooth Low Energy module based on Silicon Labs EFR32BG22 SoC.
It features a 76.8 MHz ARM Cortex-M33 processor with DSP instructions and
floating-point unit.

Features:
- EFR32BG22C224F512IM40 SoC
- 512 KB Flash memory
- 32 KB RAM
- Bluetooth 5.2 Low Energy
- 2.4 GHz radio
- ARM Cortex-M33 core
- Built-in security features

Hardware
********

The BGM220P module includes:
- ARM Cortex-M33 running at 76.8 MHz
- 512 KB of flash memory
- 32 KB of RAM
- Bluetooth 5.2 Low Energy radio
- Multiple GPIO pins
- UART, I2C, SPI interfaces
- ADC, PWM, and timer peripherals

Supported Features
******************

The bgm220p_efr32bg22 board configuration supports the following hardware features:

+-----------+------------+-------------------------------------+
| Interface | Controller | Driver/Component |
+===========+============+=====================================+
| NVIC | on-chip | nested vector interrupt controller |
+-----------+------------+-------------------------------------+
| UART | on-chip | serial port-polling; |
| | | serial port-interrupt |
+-----------+------------+-------------------------------------+
| GPIO | on-chip | gpio |
+-----------+------------+-------------------------------------+
| I2C | on-chip | i2c port-polling |
+-----------+------------+-------------------------------------+
| SPI | on-chip | spi port-polling |
+-----------+------------+-------------------------------------+
| FLASH | on-chip | flash |
+-----------+------------+-------------------------------------+
| RADIO | on-chip | Bluetooth |
+-----------+------------+-------------------------------------+

Programming and Debugging
*************************

Flashing
========

The BGM220P can be flashed using J-Link or OpenOCD.

Using J-Link:

.. code-block:: console

   west flash --runner jlink

Using OpenOCD:

.. code-block:: console

   west flash --runner openocd

Debugging
=========

Use GDB for debugging:

.. code-block:: console

   west debug
### Step 5: Build and Test
#### Basic Build Test
# Navigate to your project directory
cd ~/zephyrproject/zephyr/bgm220p_test

# Build with your new board
west build -b bgm220p_efr32bg22 --pristine

# If successful, flash to device
west flash
#### Create Test Application
// src/main.c - Simple test application
#include <zephyr/kernel.h>
#include <zephyr/device.h>
#include <zephyr/drivers/gpio.h>
#include <zephyr/drivers/uart.h>
#include <zephyr/bluetooth/bluetooth.h>
#include <zephyr/bluetooth/hci.h>

#define LED0_NODE DT_ALIAS(led0)
#define BUTTON0_NODE DT_ALIAS(sw0)

static const struct gpio_dt_spec led = GPIO_DT_SPEC_GET(LED0_NODE, gpios);
static const struct gpio_dt_spec button = GPIO_DT_SPEC_GET(BUTTON0_NODE, gpios);

void main(void)
{
    int ret;

    printk("BGM220P EFR32BG22 Board Test\n");

    /* Initialize LED */
    if (gpio_is_ready_dt(&led)) {
        gpio_pin_configure_dt(&led, GPIO_OUTPUT_ACTIVE);
        gpio_pin_set_dt(&led, 1);
    }

    /* Initialize Button */
    if (gpio_is_ready_dt(&button)) {
        gpio_pin_configure_dt(&button, GPIO_INPUT);
    }

    /* Initialize Bluetooth */
    ret = bt_enable(NULL);
    if (ret) {
        printk("Bluetooth init failed (err %d)\n", ret);
    } else {
        printk("Bluetooth initialized\n");
    }

    while (1) {
        /* Toggle LED */
        gpio_pin_toggle_dt(&led);

        /* Check button */
        if (gpio_pin_get_dt(&button) == 0) {
        printk("Button pressed!\n");
        }

        k_sleep(K_MSEC(1000));
    }
}
## Troubleshooting
### Common Issues
1. Build Errors: Check that all required files are in place
2. Flash Errors: Verify J-Link/OpenOCD connection
3. Bluetooth Issues: Ensure proper antenna connection
4. GPIO Problems: Check pin assignments in DTS file
### Validation Steps
1. Basic Boot: Device should boot and print to console
2. GPIO Test: LED should blink, button should respond
3. Bluetooth Test: Should initialize without errors
4. Flash Test: Should be able to read/write flash
5. Power Test: Check power consumption
## Next Steps
1. Submit to Zephyr: Consider contributing your port upstream
2. Add More Features: Implement additional peripheral drivers
3. Power Management: Add low-power mode support
4. Bootloader: Configure MCUboot for OTA updates
5. Testing: Create comprehensive test suite
## References
- Zephyr Board Porting Guide
- BGM220P Datasheet
- EFR32BG22 Reference Manual
- Zephyr Device Tree Guide